## Slide 1: Efficient Use Of Networks Using Network Coding

## Slide 2: What is Network Coding?
Notes: It is a fairly new term. It basically refers to combining packets together on the network and forwarding them!

## Slide 5
Combine incoming packets into one or many outgoing packets.
Goal
  Increase throughput
  Decrease Energy Consumption
  Decrease Delay/Wait Time
  Increase Reliability

## Slide 6: Increased Throughput
Increase Information Content Of Transfers And Packets.
Decreases Number Of Transfers To Transfers to Carry Data to Multiple or Single Nodes.
This Makes Bandwidth available for other nodes to use
Delay is reduced drastically.

## Slide 7: Flexibility
All packets become equally important as information gets disseminated.
Information can be retrieved by collecting enough number of packets regardless of which packets.

## Slide 8
Not only the shortest path is used but also other paths are used to transmit the data.
The traffic in the network is distributed to multiple links and network coding can have an effect of load balancing.

## Slide 9: Disadvantages
The loss of one packet could affect many other packets and renders some information useless at the receiver.
Data cannot be recovered until all
the information necessary is received  Delay

## Slide 10
Synchronization is a problem that needs to be considered when network coding will be implemented in computer or satellite networks.
It it can be a serious problem for real-time applications (e.g. voice and video transmission).
However, certain types of networks like switching networks are inherently fully synchronized. These types of networks are perfect candidates for the application of network coding.

## Slide 11: Index Coding
Works on the notion of side information.
Basically, information know to a node but not really required to the node.
This is due to the nature of the broadcast spectrum.

## Slide 16: Analog Network Coding
Instead of avoiding interference, we exploit the interference.
Multiple senders transmit simultaneously, the packets collide.
It means that the channel adds their physical signals after applying attenuations and time shifts.
Thus if we know the content of the packet that interfered we can derieve the signal we are interested in.

## Slide 20: Flooding
Flooding is a simple routing technique in computer networks where a source or node sends packets through every outgoing link.
Flooding, which is similar to broadcasting, occurs when source packets (without routing data) are transmitted to all attached network nodes.
Because flooding uses every path in the network, the shortest path is also used.

## Slide 22: All Static Nodes

## Slide 23: 40 Static Nodes
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0 | 12974 | 11921 | 763 | 84 | 84 | 84 | 0.776938
0.1 | 12974 | 11921 | 763 | 84 | 84 | 84 | 0.776938
0.2 | 12974 | 11921 | 763 | 84 | 84 | 84 | 0.776938
0.3 | 25507 | 15939 | 9069 | 164 | 164 | 164 | 0.771553
0.4 | 31870 | 5419 | 25902 | 250 | 234 | 250 | 0.921243
0.5 | 32682 | 1621 | 30617 | 250 | 250 | 250 | 0.917936
0.6 | 33908 | 38 | 33119 | 250 | 249 | 250 | 0.883567

## Slide 24: 40 Static Nodes
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0.3 | 25507 | 15939 | 9069 | 164 | 164 | 164 | 0.771553
0.31 | 24987 | 14845 | 9592 | 161 | 159 | 161 | 0.77
0.32 | 24973 | 13882 | 10647 | 161 | 161 | 161 | 0.773636
0.33 | 25837 | 14349 | 11000 | 169 | 169 | 169 | 0.784921
0.34 | 26171 | 13627 | 12107 | 149 | 170 | 149 | 0.715296
0.35 | 30616 | 13893 | 15922 | 222 | 222 | 222 | 0.870133
0.36 | 31987 | 14017 | 17239 | 233 | 240 | 233 | 0.882859
0.37 | 32392 | 12204 | 19464 | 250 | 238 | 250 | 0.911336
0.38 | 31885 | 8397 | 22788 | 250 | 222 | 250 | 0.905755
0.39 | 32274 | 6705 | 24852 | 250 | 238 | 250 | 0.914668
0.4 | 31870 | 5419 | 25902 | 250 | 234 | 250 | 0.921243

## Slide 25: 80 Static Nodes
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0 | 2053 | 1264 | 787 | 1 | 1 | 1 | 0.116902
0.1 | 2053 | 1264 | 787 | 1 | 1 | 1 | 0.116902
0.2 | 2053 | 1264 | 787 | 1 | 1 | 1 | 0.116902
0.3 | 2354 | 1272 | 1074 | 2 | 2 | 2 | 0.203908
0.4 | 67116 | 12235 | 54254 | 250 | 250 | 250 | 0.893975
0.5 | 67700 | 3645 | 63580 | 250 | 250 | 250 | 0.886263
0.6 | 68877 | 153 | 68043 | 250 | 250 | 250 | 0.871118

## Slide 26: 80 Static Nodes
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0.4 | 31870 | 5419 | 25902 | 250 | 234 | 250 | 0.921243
0.41 | 32088 | 4644 | 26867 | 248 | 235 | 249 | 0.912491
0.42 | 32248 | 4082 | 27604 | 250 | 237 | 250 | 0.914165
0.43 | 32246 | 3396 | 28352 | 250 | 233 | 250 | 0.90926
0.44 | 31926 | 3110 | 28340 | 250 | 233 | 250 | 0.918374
0.45 | 32177 | 2922 | 28810 | 250 | 238 | 250 | 0.917425
0.46 | 32196 | 2616 | 29146 | 250 | 240 | 250 | 0.919369
0.47 | 32127 | 2347 | 29361 | 249 | 242 | 249 | 0.921343
0.48 | 32134 | 2463 | 29271 | 249 | 236 | 249 | 0.913674
0.49 | 32223 | 2142 | 29620 | 249 | 240 | 249 | 0.916116
0.5 | 32682 | 1621 | 30617 | 250 | 250 | 250 | 0.917936

## Slide 27: 120 Static Nodes
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0 | 2208 | 1264 | 942 | 1 | 1 | 1 | 0.163043
0.1 | 2208 | 1264 | 942 | 1 | 1 | 1 | 0.163043
0.2 | 2208 | 1264 | 942 | 1 | 1 | 1 | 0.163043
0.3 | 4887 | 3052 | 1828 | 2 | 2 | 2 | 0.14733
0.4 | 102552 | 20198 | 81752 | 250 | 250 | 250 | 0.877604
0.5 | 102955 | 4890 | 97622 | 250 | 250 | 250 | 0.874168
0.6 | 104396 | 346 | 103349 | 250 | 250 | 250 | 0.862102

## Slide 28: 120 Static Nodes
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0.4 | 102552 | 20198 | 81752 | 250 | 250 | 250 | 0.877604
0.41 | 34699 | 6877 | 27632 | 78 | 78 | 78 | 0.809245
0.42 | 102781 | 13241 | 89072 | 250 | 247 | 250 | 0.872146
0.43 | 102870 | 9939 | 92436 | 250 | 249 | 250 | 0.873724
0.44 | 102448 | 8114 | 93859 | 250 | 248 | 250 | 0.876152
0.45 | 103061 | 9210 | 93360 | 250 | 250 | 250 | 0.873269
0.46 | 102986 | 7772 | 94709 | 250 | 250 | 250 | 0.873905
0.47 | 45084 | 4341 | 40538 | 110 | 109 | 110 | 0.875699
0.48 | 103185 | 6213 | 96558 | 250 | 250 | 250 | 0.87222
0.49 | 102790 | 6462 | 95934 | 250 | 250 | 250 | 0.875572
0.5 | 102955 | 4890 | 97622 | 250 | 250 | 250 | 0.874168

## Slide 29: Few Nodes Moving

## Slide 30: 40 Nodes
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0 | 8213 | 6627 | 1505 | 26 | 26 | 26 | 0.379886
0.1 | 8338 | 6750 | 1509 | 26 | 26 | 26 | 0.37419
0.2 | 8149 | 6569 | 1515 | 24 | 24 | 24 | 0.353418
0.3 | 5801 | 3073 | 2725 | 2 | 2 | 2 | 0.041372
0.4 | 7756 | 1711 | 5945 | 24 | 24 | 24 | 0.371325
0.5 | 12200 | 1101 | 10946 | 64 | 63 | 64 | 0.62623
0.6 | 12584 | 50 | 12354 | 64 | 64 | 64 | 0.610299

## Slide 31
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0.3 | 5801 | 3073 | 2725 | 2 | 2 | 2 | 0.041372
0.31 | 4648 | 2692 | 1956 | 2 | 2 | 2 | 0.051635
0.32 | 5237 | 2067 | 3167 | 2 | 2 | 2 | 0.045828
0.33 | 4881 | 1713 | 3166 | 2 | 2 | 2 | 0.04917
0.34 | 5294 | 1684 | 3607 | 2 | 2 | 2 | 0.045334
0.35 | 5175 | 1577 | 3594 | 2 | 2 | 2 | 0.046377
0.36 | 5632 | 1595 | 4033 | 2 | 2 | 2 | 0.042614
0.37 | 7246 | 2374 | 4783 | 23 | 23 | 23 | 0.3809
0.38 | 7924 | 2361 | 5467 | 26 | 26 | 26 | 0.393741
0.39 | 7818 | 1900 | 5820 | 22 | 26 | 22 | 0.358148
0.4 | 7756 | 1711 | 5945 | 24 | 24 | 24 | 0.371325
40 Nodes

## Slide 32: 80 Nodes
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0 | 10705 | 8865 | 1788 | 21 | 21 | 21 | 0.470808
0.1 | 10728 | 8900 | 1776 | 21 | 21 | 21 | 0.469799
0.2 | 10728 | 8820 | 1816 | 21 | 21 | 21 | 0.469799
0.3 | 6106 | 3129 | 2975 | 2 | 2 | 2 | 0.078611
0.4 | 19324 | 3533 | 15654 | 58 | 57 | 58 | 0.716208
0.5 | 19844 | 749 | 18997 | 58 | 59 | 58 | 0.705503
0.6 | 20219 | 29 | 20039 | 59 | 59 | 59 | 0.700331

## Slide 33
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0.3 | 6106 | 3129 | 2975 | 2 | 2 | 2 | 0.078611
0.31 | 5577 | 2463 | 3112 | 2 | 2 | 2 | 0.086068
0.32 | 5751 | 2709 | 3040 | 2 | 2 | 2 | 0.083464
0.33 | 5926 | 2356 | 3568 | 2 | 2 | 2 | 0.080999
0.34 | 5908 | 2199 | 3707 | 2 | 2 | 2 | 0.081246
0.35 | 5912 | 1868 | 4042 | 2 | 2 | 2 | 0.081191
0.36 | 5578 | 1471 | 4104 | 2 | 2 | 2 | 0.086052
0.37 | 18572 | 7901 | 10505 | 48 | 53 | 53 | 0.663364
0.38 | 19034 | 5570 | 13310 | 54 | 55 | 56 | 0.693496
0.39 | 18663 | 6157 | 12290 | 59 | 59 | 58 | 0.754434
0.4 | 19324 | 3533 | 15654 | 58 | 57 | 58 | 0.716208
80 Nodes

## Slide 34: 120 Nodes
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0 | 8213 | 6627 | 1505 | 26 | 26 | 26 | 0.379886
0.1 | 8338 | 6750 | 1509 | 26 | 26 | 26 | 0.37419
0.2 | 8149 | 6569 | 1515 | 24 | 24 | 24 | 0.353418
0.3 | 5801 | 3073 | 2725 | 2 | 2 | 2 | 0.041372
0.4 | 7756 | 1711 | 5945 | 24 | 24 | 24 | 0.371325
0.5 | 12200 | 1101 | 10946 | 64 | 63 | 64 | 0.62623
0.6 | 12584 | 50 | 12354 | 64 | 64 | 64 | 0.610299

## Slide 35
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0.4 | 12626 | 3080 | 9465 | 23 | 14 | 17 | 0.513227
0.41 | 30049 | 5554 | 24294 | 68 | 61 | 64 | 0.770741
0.42 | 31828 | 4472 | 27220 | 70 | 70 | 70 | 0.791756
0.43 | 31887 | 4228 | 27521 | 70 | 70 | 70 | 0.790291
0.44 | 31798 | 3530 | 28157 | 70 | 70 | 70 | 0.792503
0.45 | 32257 | 2723 | 29380 | 70 | 71 | 71 | 0.788666
0.46 | 31778 | 3002 | 28657 | 69 | 70 | 70 | 0.789225
0.47 | 32212 | 2243 | 29838 | 71 | 71 | 70 | 0.789768
0.48 | 31880 | 2130 | 29633 | 69 | 70 | 70 | 0.7867
0.49 | 32395 | 1998 | 30281 | 71 | 71 | 71 | 0.789011
0.5 | 31877 | 1870 | 29891 | 70 | 70 | 69 | 0.786774
120 Nodes

## Slide 36: Increase In Range

## Slide 37: 40 moving nodes
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0 | 17971 | 15957 | 1768 | 24 | 152 | 25 | 0.447387
0.1 | 17971 | 15957 | 1768 | 24 | 152 | 25 | 0.447387
0.2 | 13069 | 10911 | 2048 | 15 | 85 | 15 | 0.351978
0.3 | 18607 | 10445 | 7910 | 107 | 12 | 109 | 0.490138
0.4 | 25470 | 6218 | 18871 | 167 | 186 | 167 | 0.816647
0.5 | 28646 | 3168 | 25068 | 202 | 212 | 202 | 0.860155
0.6 | 33947 | 62 | 33118 | 249 | 249 | 249 | 0.880196
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0 | 8213 | 6627 | 1505 | 26 | 26 | 26 | 0.379886
0.1 | 8338 | 6750 | 1509 | 26 | 26 | 26 | 0.37419
0.2 | 8149 | 6569 | 1515 | 24 | 24 | 24 | 0.353418
0.3 | 5801 | 3073 | 2725 | 2 | 2 | 2 | 0.041372
0.4 | 7756 | 1711 | 5945 | 24 | 24 | 24 | 0.371325
0.5 | 12200 | 1101 | 10946 | 64 | 63 | 64 | 0.62623
0.6 | 12584 | 50 | 12354 | 64 | 64 | 64 | 0.610299
72 vs 80

## Slide 38
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0.3 | 5801 | 3073 | 2725 | 2 | 2 | 2 | 0.041372
0.31 | 4648 | 2692 | 1956 | 2 | 2 | 2 | 0.051635
0.32 | 5237 | 2067 | 3167 | 2 | 2 | 2 | 0.045828
0.33 | 4881 | 1713 | 3166 | 2 | 2 | 2 | 0.04917
0.34 | 5294 | 1684 | 3607 | 2 | 2 | 2 | 0.045334
0.35 | 5175 | 1577 | 3594 | 2 | 2 | 2 | 0.046377
0.36 | 5632 | 1595 | 4033 | 2 | 2 | 2 | 0.042614
0.37 | 7246 | 2374 | 4783 | 23 | 23 | 23 | 0.3809
0.38 | 7924 | 2361 | 5467 | 26 | 26 | 26 | 0.393741
0.39 | 7818 | 1900 | 5820 | 22 | 26 | 22 | 0.358148
0.4 | 7756 | 1711 | 5945 | 24 | 24 | 24 | 0.371325
Threshold | Packets in network | Coded Packets | Non-Coded Packets | Destination 1 Unique | Destination 2 Unique | Destination 3 Unique | Ratio
0.3 | 18607 | 10445 | 7910 | 107 | 12 | 109 | 0.490138
0.31 | 19199 | 10450 | 8428 | 98 | 66 | 97 | 0.543778
0.32 | 21712 | 11914 | 9462 | 143 | 74 | 142 | 0.661385
0.33 | 22789 | 11818 | 10618 | 107 | 133 | 105 | 0.605555
0.34 | 25751 | 12667 | 12518 | 190 | 154 | 190 | 0.829482
0.35 | 26583 | 13214 | 12853 | 184 | 173 | 184 | 0.814054
0.36 | 23479 | 9695 | 13387 | 150 | 140 | 152 | 0.753013
0.37 | 26761 | 11296 | 14922 | 163 | 201 | 163 | 0.787713
0.38 | 26315 | 8849 | 16954 | 169 | 190 | 169 | 0.802584
0.39 | 24881 | 6735 | 17669 | 179 | 158 | 179 | 0.829549
0.4 | 25470 | 6218 | 18871 | 167 | 186 | 167 | 0.816647
72 vs 80

## Slide 39: Applications!

## Slide 40: P2P Networks
A server distributes a ﬁle by breaking it down into small blocks.
Clients in turns, download those small blocks from the server and distribute them among their neighbors.
Network coding has been used in a P2P prototype called Avalanche developed by Microsoft where the blocks sent by servers and clients are random combinations of original blocks.

## Slide 41: P2P Networks
Server divides files into smaller blocks. (B1,B2,B3,B4,…,Bn.)
Client now receives a linear combination of these blocks.
A coeﬃcient vector u is sent for the client to be able to decode the original blocks.

## Slide 42: COPE: Packet-level Network Coding
It takes advantage of the broadcast nature of the wireless medium, which allow multiple nearby nodes to overhear a packet when it is broadcast from a node.

## Slide 43: Network Coding In security
Network coding has been shown to improve security against many types of attacks including: eavesdropping, modifying data, and jamming attack.
Data does not exist on one node but rather is distributed, overhearing data packets will not result in getting the information except by getting all the required blocks which makes it harder for the eavesdropper
Due to data distribution we can know any piece that was changed, which prevents against modification attacks.

## Slide 44: Conclusion
Network Coding is a new and promising area which is based on computer and communication network problems.
Using network coding could help improve performance of a networks by exploiting current infrastructure.
Compared to traditional routing, Network Coding offers more benefits with respect to resource, efficiency and robustness.

## Slide 45: How Did I Enjoy Japan?

## Slide 47: Thank You